## Slide 1: iSHELL Design Review Cryostat & Optics Bench
Dan Kokubun
11/8/2013

## Slide 2: Overview
3/8” tapped holes on covers, bottom, and sides.
Can be used for:
handles
Jigs
protective frame
feet.

## Slide 3: Overview – Telescope Clear Envelope
Telescope clear envelope shown around instrument.
Estimated Weight: 1040 lbs
CG: within 2” of optical axis
Clear Envelope

## Slide 4: Overview
LN Can
Aladdin
Cal Box
Aladdin
Controller
Rotator Mechanism
Cal Box dust cover not shown

## Slide 5: Overview
X Disperser
Mechanism
IG Changer
*upgrade
Cal Box
H2RG
Controller
H2RG
Order Sorting
Mechanism
Cal Box dust cover not shown

## Slide 6: FEA - Flexure Study
Chart: Image Displacement at Secondary Telescope Pointing - 60 deg from Zenith
| 0 | 45 | 90 | 135 | 180 | 225 | 270 | 315 | 360
dY Component' | -0.023739 | 0.3314 | 0.53472 | 0.39975 | -0.011911 | -0.44856 | -0.61435 | -0.39204 | -0.023739
dX Component | 0.48972 | 0.32475 | -0.017177 | -0.355 | -0.49311 | -0.33554 | 0.016023 | 0.34941 | 0.48972
dTotal' | 0.49029 | 0.46399 | 0.535 | 0.53462 | 0.49326 | 0.56017 | 0.61456 | 0.52515 | 0.49029
Requirement: Co-alignment of the cold stop and telescope exit pupil to within 1% of their diameters...
This is equivalent to 2.4mm image displacement at the secondary
Worst case gravity vectors used (60° from zenith)
The resulting angular deflection of the optical axis is expressed as image displacement at the secondary
Maximum contribution is 0.61 mm ; 25% of the allowable displacement
Includes Contributions From:
Telescope Mount
Cryostat
Trusses
Optical Bench
N
E
S
W
N

## Slide 7: FEA - Stiffness Under Vacuum
Maximum deflection at center of cover is 1.2mm

## Slide 8: FEA - Stiffness Under Vacuum
Maximum stress at ribs on cover is < 15 kpsi; safety margin of 2.7 for 6061-T6
Stress points on bottom around 11 kpsi; safety margin of 2 for 50XX-T0

## Slide 9: Cryostat - Housing
Welded Structure (welds shown in red)
Cryostat design has been developed in cooperation with the cryostat vendor.
Parts milled from billet
Inserts for Truss mounts screwed in place
Will use 5083-T0 or 5056-T0 to avoid heat treating
Elastic Modulus for all alloys are about the same so deflections will be identical
Inside surfaces are polished
Outside surfaces are painted
 | Tensile Yield | Notes
AL 5083-T0 | 21 kpsi | No heat treat
AL 5056-T0 | 22 kpsi | No heat treat
AL 6061-T6 | 40 kpsi | Heat treat required post welding. Severe warping expected

## Slide 10: Cryostat Cover
Step on cover supports walls under vacuum
Dovetail O-ring groove to retain o-ring.
O-ring groove in cover
3/16” dia o-rings

## Slide 11: Cryostat Vendor – Meyer Tool & Manufacturing
AURA One Degree Instrument (ODI)
Vacuum rated welds
O-ring grooves with dovetail
Large Capacity Milling Machines
Vacuum testing capability

## Slide 12: Cryostat - Window
Window mount is inset to allow space for a gas tube used for calibration
A motorized door covers the window when it is not in use
Debris cup to be installed on the back of the fold mirror
Window bezel reduces the amount of debris falling onto window.

## Slide 13: Cryostat – Warm Side Truss Mounts
Warm Side Mount
  Custom shoulder screw
  Use loose fitting threads for better fitment
  Stainless insert in cryostat wall
Custom Shoulder Screw
Stainless Insert
Cryostat
Radiation
Shield
Truss
Truss

## Slide 14: Cryostat – Cold Side Truss Mounts
Cold Side
  Two 3/8” pins, two ¼-20 screws
  Stainless insert in bench with clocking pin
Cold Bench
Radiation Shield
Cryostat
Truss
Stainless Insert
Truss
3/8” pins
¼-20 tapped holes
Stainless Insert

## Slide 15: Cryostat – Radiation Shield
Truss Clearance Slots
With Covers (4x)
Truss Mount Bolt
Access Covers (8x)
Wire Harness
Access Panels (3x)
G-10 Mount Tabs (4x)
1.9W Heat Load – similar to Spex
Lower Support Assembly
Lower Support Assembly
Support pin mounted to the cryostat will provide mechanical support to the bottom of the radiation shield
Small thermal cross section at bearing surface
G-10 Spokes (4x)
Support Pin
Bearing Surface

## Slide 16: Optics Bench
Photon Shield
Spectrometer
Photon Shield
Foreoptics
LN Can
Bench
Bus Bar

## Slide 17: Optics Bench – Wire Routing
All wires in covered channels
Motor power and heater wires routed together
Hall effect sensors and temperature sensors routed together
Light tight bulkhead connectors
Foreoptics
Spectrograph
IG Mech
Slit Wheel
Dekker Mech
X Disperser Mech
OS Mech
Filter Wheel
Rotator
Filter Wheel
Rotator
Motor and Heater Power
Position and Temp Sense

## Slide 18: Optics Bench – Connectors
Aladdin Sensor
External access to wire harnesses
Hermetic connectors epoxied to a single plate
Radiation shield access panel
Epoxied bulkhead headers on the bench wall
Hall Effect Sense
Temp Sense

## Slide 19: Optics Bench – Photon Shield
Welded Pan (3mm thk)
Machined Flange
Pan welded to flange
Painted inside, polished outside
Qty 31 of #10 captive screws (~4” spacing)
Guide pins used to align tongue and groove during installation

## Slide 20: Thermal Design – Hybrid Overview
LN Cooled Bench
CCC First Stage Cooled
Radiation Shield
CCC Second Stage Cooled
Aladdin and H2RG

## Slide 21: Thermal Design – LN Can
LN Can – milled from billet and welded
LN Neck – Welded bellows, stainless tubes
Cooling Bus Bar mouned with G-10 tabs
Bus Bar Feedthru epoxied to G-10 disk
Bus Bar Feed Thru

## Slide 22: Assembly
Install radiation shield in cryostat
Install bench with trusses
Install truss covers
Install wire harnesses and radiation shield access panels (not shown)
Install cryo cooler and thermal straps
Install mechanisms and optics (not shown)
Install photon shields
Install remainder of radiation shield mount tabs and radiation shield panels
Install cryostat covers
Install array controllers
1
2
7
8
9
8
7
10
5
3
9